## Slide 1: Cool Arduino projekti
Tomislav Teskač
Kristian Dekarin

## Slide 2: Agenda
Arduino & IOT
How to start? What do I need? How much does it cost?
Arduino I klonovi
Senzori, aktulatori, motori
IDE -Visual studio Micro, Atmel studio, Arduino
Example projekta: Dron i autic

## Slide 3: SparkFun & Adafruit - “low cost, simple tools for non-engineers to create digital projects”
Open sourced h/s microcontroler
Arduino extensions, shields?
How to write Sketch: AVR Studio, Atmel Studio, Arduino IDE, VS Micro
Arduino in numbers:
Downloaded x times
Sketch basic functions:
Arduino in numbers:
2011 - 300 000
2013 - 700 000

## Slide 4
Arduino Nano, Uno, Due?
Clone or original

## Slide 7: Used for? 2009 -> NASA
* A joke 

## Slide 8: Used for?
Display LCD (weather, notes)
Any kind of toy (electronic piano,Wifi controller RC)
Alarm
Smart phone dore opener
Lamps
Home automatization Server
Email notifier
Maze Solver Robot
More @: http://playground.arduino.cc/Projects/Ideas

## Slide 9: Used with:
Boards,
Lipos > Checker,
Connectors,
Wires + (crocodile wires)
Lemilica… ?
JoyStick Module
Potentiometer
Transmiter -> Reciver, ESC8266, Bluetooth
Hbridge
Servo – Steper Motors,
KeyPad membrane
Buzzers
LCDs,
Temp sensor
LEDs Strip…

## Slide 10: Example projekta Arduino servo
#include <SoftwareSerial.h>
#include <Servo.h>
Servo myservo; // create servo object to control a servo
// twelve servo objects can be created on most boards
int pos = 0; // variable to store the servo position
void setup() {
myservo.attach(9); // attaches the servo on pin 9 to the servo object
}
void loop() {
for (pos = 0; pos <= 180; pos += 1) { // goes from 0 degrees to 180 degrees
// in steps of 1 degree
myservo.write(pos); // tell servo to go to position in variable 'pos'
delay(15); // waits 15ms for the servo to reach the position
}
for (pos = 180; pos >= 0; pos -= 1) { // goes from 180 degrees to 0 degrees
myservo.write(pos); // tell servo to go to position in variable 'pos'
delay(15); // waits 15ms for the servo to reach the position
}
}

## Slide 11: VS Micro & Arduino IDE
The gcc toolchain consists of all tools that run in the background if you select "build" or "upload" commands.

## Slide 12: VS Micro Vs Arduino
VS Micro
intellisense
Can be used in VS and Atmel
The breakpoint location might be invalid?
Error handling: expected ';' before '}‘
Formated code
File as Libary in solution
Global rename
Auto reconnect, logging...
Arduino
+LightWeight (fast)
+Simple
"Provides an advanced and professional development environment, and allows for more advanced development than the existing Arduino IDE"

## Slide 13: VS Micro – Installation / Configuration
Get Arduino and cabel
Install arduino IDE
VS Community (08-15) -> NOT Express

## Slide 14: Example projekta Samohodni Autic
Demo
https://youtu.be/Q1L_YQG4v_o
C:\Users\kdeka\OneDrive\Documents\1. Development\_Arduino prezentation\vids

## Slide 17: Kako sam naučio Arduino?
aa

## Slide 18: Istraživanje komponenata

## Slide 19: Dizajn #1

## Slide 20: Dizajn #2

## Slide 21: Dizajn #3

## Slide 22: Dizajn #4

## Slide 24: Demo
Video #1
Video #2
Video #3
Uživo 

## Slide 25: Demo
Video #1
Video #2
Video #3
Uživo 

## Slide 26: Problemi
Problem #1 – „Vaga”- PID Controller
Problem #2 – Komunikacija s Arduinom
Problem #3 – PWM/PPM signal
Problem #4 – Koliko ima digitalnih izlaza?
Problem #5 - Pull-Up/Pull-Down Resistors

## Slide 27: Problem #1 – „Vaga”- PID Controller

## Slide 28: Problem #2 – Komunikacija s Arduinom
- Istovremeno čitanje dolaznih podataka s WiFi-a i stabilizacija
- Delay nakon čitanja serial.Read() ili serial.Available()
- Multithreading?
- Čitaj samo jedan character po ciklusu „loop()” funkcije
:50 50 50 0;
:50 50 50 1;
:50 50 50 2;
...
:50 50 50 30;
:51 50 50 30;
:52 50 50 30;
...
:60 50 50 30;
:60 51 50 30;
:60 52 50 30;
...
:50 60 50 30;
…

## Slide 30: Problem #2 – Komunikacija s Arduinom
- 3.3v regulator
- ESP8266 current: 250mA
- Arduino 3.3v = max 150mA

## Slide 31: Problem #3 – PWM/PPM signal
- PWM je analogni digitalni signal
- Pulse Width Modulation vs Pulse Position Modulation
- 6 PWM izlaza na 3 interna timera PPM
  Pin 5 i 6: timer0
  Pin 9 i 10: timer1
  Pin 3 i 11: timer2

## Slide 32: Problem #4 – Koliko ima digitalnih izlaza?
- Kako upravljati s mnogo više digitalnih izlaza nego što ih ima Arduino?
- Demultipleksor
- Shift registri

## Slide 33: Prob. #4 – Shift Register

## Slide 34: Trik #1 – Koliko ima digitalnih izlaza?

## Slide 35: Problem #5 - PullUp/PullDown otpornici
a

## Slide 36: Ideje za projekte
- Autonomni autić
- Dronovi
- Display pomoću shift registara
- LED traka aktivirana po zvuku
- HDD laser projektor
- PIR WiFi alarm

## Slide 37: Što od el. komponenata je dobro imati?
- Arduino 
- Step-Up converter
- Step-Down converter
- 5v regulatori
- 3.3v regulatori
- TIP122 tranzistori
- ESP8266 (koji i koje su prednosti u odnosu na druge modele)
- Senzori

## Slide 38: Oprez!
- Ako kontrolirate nešto „opasno” pomoću mobitela stavite ga u airplane mod! Zašto? Da vas netko ne nazove u kritičnoj situaciji 

## Slide 39: Ako bude vremena 
- Načini komunikacije među više arduina.
  Wifi, bluetooth,
  serial, software serial
  I2C, PPM
- LiPo baterije - koliko su jake i opasne, koliku struju mogu davati
  1300mAh * 40C = 52000mAh = 52A
- Razlika: stepper vs servo motor
  Servo zna gdje se nalazi i koliko je okrenut a stepper je „glup”
- Upravljanje motorom u 2 smjera
  H bridge

## Slide 40: return 0; //Success